## Slide 1: A Combined Electromagnetic Induction-Magnetometer Sensing Approach for Detecting Subsurface Targets
Max Orman-Kollmar1, Randall Reynolds2, Rui Zhang3, Ben Barrowes2, Fridon Shubitidze1
1Thayer School of Engineering, Dartmouth College, Hanover NH USA
2Cold Regions Research and Engineering Lab, Hanover NH USA
3Geometrics Inc., San Jose, CA USA

## Slide 2: Outline
Motivation
Overview of Magnetometers and EMI
Preliminary Expectations
Testing Process
Data Collected
Q&A

## Slide 3: Motivation
There are well-established sensors that are used for subsurface investigations:
Magnetometers
Electromagnetic Induction Sensors
These (and other) sensors are often used “independently”.
Notes: Many well-established sensors used for subsurface investigations, whether that is in the realm of UXO detection, infrastructure mapping, or ground stability investigations. Two among them are magnetometers and electromagnetic induction sensors. Each of these has its own specific use cases, as well as limiting factors.

## Slide 4: Magnetometers
Passive sensors
Total field, gradient, or vector components of magnetic field
Detect “magnetic anomalies” for limited number of target types
Atomic magnetometers have high sensitivity
http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/MagEarth.html
Notes: Magnetometers are primarily PASSIVE sensors, picking up “local anomalies” in Earth’s constant magnetic field. They come in different sensing iterations- whether they sense the total magnetic field, a gradient of the field over an area, or recording the components of the magnetic field in the cartesian directions. In the last few years, the developed atomic magnetometers have high sensitivity, down to the tens of nanotesla for field detections. However, the detected magnetic anomalies are for a “limited” number of targets.
Image credit: http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/MagEarth.html

## Slide 5: Electromagnetic Induction
Combination of active and passive components
Works on conducting targets, not just ferrous/ferromagnetic
Limited sensing depth

## Slide 6: Motivation Revisited
Magnetometers:
Due to their high sensitivity, magnetometers are useful for detecting small or deep targets
Magnetometers are able to pick up on the anomalies in the local magnetic field in the case of ferromagnetic targets
Electromagnetic Induction Sensors
EMI signal is very strong at early times due to measuring dB/dt
EMI sensors can pick up anomalies for conducting targets in general
There is a need to improve detection depth of electromagnetic systems. Much work has been put into improving individual sensor types. But what other potential improvement methods are there?
Notes: CLARIFY WHY DB/DT IS SMALL AT LATE TIME VS MAGNETIC FIELD
INCLUDE FIGURE SHOWING (TIME VS MAGNETIC FIELD) AND (TIME VS DB/DT)
CAN GET RESPONSES FROM DFLAG0 AND DFLAG1

## Slide 7: Motivation (cont.)

## Slide 8: Can a combination of the magnetometers and EMI provide more information?
Would excitation of a target with an EMI transmitter allow for seeing these targets’ responses in later time channels in a magnetometer?
Would the EMI excitation allow a magnetometer to see nonferrous targets?

## Slide 9: Expectations
Understanding the expected response of a target subjected to an alternating magnetic field
A Hybrid Full MAS and Combined MAS/TSA Algorithm for Electromagnetic Induction Sensing, F. Shubitidze, K. O’Neill, K. Sun, I. Shamatava, K. D. Paulsen, ACES Journal Vol 19 No 1b, March 2004
Notes: Left: non-permeable sphere
Right: highly-permeable sphere (mu_r = 50)
EMPHASIZE:
NON-PERMEABLE MATERIALS ARE SYMMETRIC BETWEEN TURN ON & TURN OFF
PERMEABLE MATERIALS ARE MAGNETIZED AFTER TURN ON; WHEN TURN OFF CASE THESE MATERIALS THEN HAVE ADDITIONAL MAGENTIZATION, SO ARE NOT SYMMETRIC RESPONSES

## Slide 10: Responses Recorded in Magnetometers
Four distinct data sets collected
  Static Background:
  Active Background:
  Static Target:
  Active Target:
The desired information is solely the response of the target due to the transmitter, and needs to be extracted:
To fully decouple the signals a vector magnetometer is needed
Notes: *** WILL NEED VECTOR FIELDS TO FULLY DECOUPLE ***
*** BECAUSE OF TIME-VARYING FIELD, EARTH’S FIELD IS CLOSE TO 0, MAKING IT EASIER TO DECOUPLE ***

## Slide 11: Testing Setup
The EMI transmitter separated vertically from both the EMI receiver and the magnetometers
Targets placed between the two at various elevations and orientations
Iron sphere
Brass ISO (Medium)
Aluminum cylinder
Notes: The intention is to see if there is a way to see data at late time. Since the magnetometers have high sensitivity, they should be able to detect low the low magnitude secondary magnetic field created from the EMI transmitter. The

## Slide 12: Targets
Medium Schedule 40 ISO Pipe Section
8” Long
2.25” Outer Diameter
0.15” Wall Thickness
* Used steel, brass, and aluminum pipes *
Aluminum Cylinder
18” Long
3” Diameter
Copper Plate
20.5” Long
4” Wide
0.25” Thick
Iron ball
4” Diameter

## Slide 13: Physical Limitations
The EMI system produces a strong magnetic field (close to the value of Earth’s magnetic field)
The atomic magnetometers function through a “calibrated” cesium vapor to detect magnetic fields and changes therein
Operating both systems simultaneously can lead to some issues in the magnetometer data
  To prevent this, need either physical separation between the sensors or limit the current used to generate the primary field

## Slide 14: Medium ISO Response Comparison
8” (20.32cm)
OD: 2.375” (6.0325cm)
ID: 2.067” (5.25cm)

## Slide 15: Medium ISO Response Comparison
8” (20.32cm)
OD: 2.375” (6.0325cm)
ID: 2.067” (5.25cm)

## Slide 16: Preliminary findings: Different Target Geometries and Compositions
18” long
3” diameter
20.5” long
4” wide
0.25” thick
Notes: Using a magnetometer, non-permeable materials are not detected usually.
However, because the MFAM has a 2kHz (relatively high) sampling rate, the magnetometer is able to record the time-varying magnetic field (as opposed to the static magnetic field typically utilized).

## Slide 17: Target Parameter Extraction
To ensure that the responses seen can be generalized, as well as making sure that the responses seen fit within reasonable expectations, a modeling approach is helpful
To correctly predict the responses, parameters for the targets used need to be identified

## Slide 18: Conclusions and Further Steps
Using magnetometers and EMI systems as complements in subsurface investigations is promising!
Offset between active EMI and magnetometers characterized.
Further modeling of targets used for comparisons to data to be implemented.
Investigating better signal decoupling using vector magnetometer at close proximity to target.

## Slide 19: Acknowledgements
This work was funded by the National Science Foundation (NSF) grant DGE2125733. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the funding organizations
Notes: NRT: Transformative Research and Graduate Education in Sensor Science, Technology and Innovation

## Slide 20: Thank you!
Any Questions?
Email: MaxOrmanKollmar.TH@dartmouth.edu