## Slide 1
Addressing Saturated Response Areas as Part of Removal Actions and Remedial Investigations at Munitions Response Sites
Presented By: Wendy Church, P.G.
SAGEEP Munitions Response Meeting
April 15, 2025
Trust. Performance. People.

## Slide 2
Weston Solutions, Inc.
Saturated Response Areas
What are they?
Saturated Response Area (SRA)
An area where anomaly selection is not possible because responses from multiple sources overlap each other to the degree that geophysical anomaly selection or source classification cannot be performed
From Engineer Manual (EM) 200-1-15
Notes: Also referred to as the Massachusetts Military Reservation

## Slide 3
Weston Solutions, Inc.
Saturated Response Areas
What are they?
Saturated Response Area (SRA)
An area where anomaly selection is not possible suspect because responses from multiple sources overlap each other to the degree that reliable geophysical anomaly selection or source classification cannot be performed.
From Engineer Manual (EM) 200-1-15
Notes: Also referred to as the Massachusetts Military Reservation

## Slide 4
Saturated Response Areas
It depends…
Weston Solutions, Inc. 4
Anomaly densities can vary
Can vary by instrument
According to EM 200-1-15
  Somewhere between 3,000 and 12,000 anomalies per acre (APA) for AGC methods
  Between 800 and 2,000 APA for non-AGC methods
Can vary based on site-specific conditions
  May be reduced in areas with large sources of MEC or MD
  Or increased in areas where small sources are present
  Depth of items is a factor

## Slide 5
Saturated Response Areas
What do we need to do?
Weston Solutions, Inc. 4
EM 200-1-15
(Section 6-8)
February 2024
RA: “SRAs must be cleared such that subsequent re-mapping using project-specific digital method(s) can discern individual sources.”
RI: “The PDT should establish decision rules for characterizing or managing SRAs and account for them in evaluating remedial alternatives in the FS.”

## Slide 6
Saturated Response Areas
What do we need to do?
Weston Solutions, Inc. 4
Final, March 2023
No SRAs in final detection survey data.
All SRAs digitally remapped to confirm anomaly densities reduced to below DQO thresholds.
SRA boundaries documented in GIS deliverable.
MR QAPP Toolkit 2: RA
(WS#12 black text)
EM 200-1-15
(Section 6-8)
February 2024
RA: “SRAs must be cleared such that subsequent re-mapping using project-specific digital method(s) can discern individual sources.”
RI: “The PDT should establish decision rules for characterizing or managing SRAs and account for them in evaluating remedial alternatives in the FS.”

## Slide 7
Saturated Response Areas
What do we need to do?
Weston Solutions, Inc. 4
Final, March 2023
No SRAs in final detection survey data.
All SRAs digitally remapped to confirm anomaly densities reduced to below DQO thresholds.
SRA boundaries documented in GIS deliverable.
MR QAPP Toolkit 2: RA
(WS#12 black text)
MR QAPP Toolkit 1: RI
EM 200-1-15
(Section 6-8)
Update 1, April 2020
?
February 2024
RA: “SRAs must be cleared such that subsequent re-mapping using project-specific digital method(s) can discern individual sources.”
RI: “The PDT should establish decision rules for characterizing or managing SRAs and account for them in evaluating remedial alternatives in the FS.”

## Slide 8
Weston Solutions, Inc.
Project plans pre-date current requirements
RI report finalized in 2014
Mostly wooded, undeveloped land
Portions of Croft State Park
  High public use areas
591 acres of APEX One-pass surveys
Former Camp Croft Maneuver Area
Removal Action

## Slide 9
Weston Solutions, Inc.
  RI Results
  Based on analog and EM61 data
  No mention of SRAs
  Highest concentrations of items in public use areas
Former Camp Croft Maneuver Area
SRA Distribution

## Slide 10
Public High-Use Areas
Saturated Response Areas
Weston Solutions, Inc.
  More extensive than expected
  Expected SRAs in public use areas
  Found more in remote areas
  55 acres were determined to be SRAs (>2,000 APA)
  SRAs identified during data analysis
  Additional SRAs delineated with GIS and Oasis Montaj
  No anomaly reduction or remapping
Former Camp Croft Maneuver Area
SRA Distribution

## Slide 11
Weston Solutions, Inc.
  Managing SRAs for next phase
  SRAs from Phase 1 will be cleared in Phase 2
    Anomaly reduction using analog sensors (to below 2,000 APA) and re-surveyed
    Possible multiple iterations
  New SRAs in Phase 2 grids will be delineated based on detection data
    Before classification are done
    Survey unit (SU) basis rather than individual grids
    Analog anomaly reduction and remapping
    No SRAs in final data
Former Camp Croft Maneuver Area
SRA Distribution

## Slide 12
Weston Solutions, Inc.
  Project 04 MRS
    Demolition Area 1
    157 acres
  Project 05 MRS
    Turret Gunnery Range
    8,468 acres
  Preliminary characterization transects
    288 ft transect spacing
    APEX One-pass
    HD delineation
    No intrusive investigation
Former Boardman AFR
Remedial Investigation

## Slide 13
Weston Solutions, Inc.
  Detailed characterization mini-grids
    44 in HD areas (50 x 50 ft)
    11 in LD areas (100 x 100 ft)
    5 acres total
  Intrusive sampling
    1,400 single point anomalies (SPAs)
Former Boardman AFR
Remedial Investigation

## Slide 14
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
  No plan in place for managing SRAs
  SRAs identified after classifications complete
  VSP analysis for individual grids
    2,000 APA for APEX One-pass
  SRAs in 10 of the 55 grids
    6 grids were 100% SRAs
    4 grids had partial SRAs
  Both grids in Project 04 MRS were 100% SRAs

## Slide 15
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
  Intrusive data from all grids, including SRAs
  1,400 anomalies
  TOI, non-TOI, Inconclusive (“cannot analyze”)
  No plan for anomaly reduction
  Added selection of SRA targets to RI dig list
    Focused on higher decision metrics
    Variety of predicted item types and depths
    Increased dig radius to 40 cm

## Slide 16
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
Grid | Percent SRA | Anomaly Density (APA)
P04-G01 | 100% | 6,813
P04-G02 | 100% | 5,105
P05-G09 | 100% | 11,238
P05-G19 | 100% | 3,746
P05-G29 | 70% | 3,206
P05-G32 | 95% | 2,858
P05-G33 | 100% | 5,384
P05-G37 | 36% | 2,178
P05-G39 | 75% | 2,631
P05-G44 | 100% | 3,154
P04-G01
P05-G09

## Slide 17
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
  Grid P04-G01 Detection Map
  15mV anomaly detection threshold
  6,813 APA based on detections
  51 targets dug
  131 items recovered
  128 MD and 1 MEC recovered
  QC seed failed offset MQO at 46 cm
  Detections are underestimating anomaly density

## Slide 18
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
  Grid P05-G09 Detection Map
  15mV anomaly detection threshold
  14 targets dug resulting in 9 “no-contacts”
  Buried electrical line
    Coherent EM noise, filter applied
  QC seed passed all MQOs
  QA and QC seeds recovered
  8 out of 9 “no-contact” digs <0.82 decision metric (stop dig threshold of 0.85)
  2 MD (20 mm projectiles)
  Detections are overestimating anomaly density

## Slide 19
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
SRA Grid | Detections | Classified Targets | % Difference
P04-G01 | 391 | 1,097 | 95%
P04-G02 | 293 | 630 | 73%
P05-G09 | 645 | 324 | -66%
P05-G19 | 215 | 436 | 68%
P05-G33 | 309 | 807 | 89%
P05-G44 | 181 | 387 | 73%

## Slide 20
Weston Solutions, Inc.
Former Boardman AFR
Remedial Investigation
SRA Grid | Detections | Classified Targets | % Difference | Targets Dug* | Items Found* | % Difference
P04-G01 | 391 | 1,097 | 95% | 51 | 131 | 88%
P04-G02 | 293 | 630 | 73% | 20 | 29 | 22%
P05-G09 | 645 | 324 | -66% | 14 | 5 | -95%
P05-G19 | 215 | 436 | 68% | 21 | 28 | 29%
P05-G33 | 309 | 807 | 89% | 25 | 31 | 21%
P05-G44 | 181 | 387 | 73% | 22 | 107 | 132%
  *Not counting seeds and corner stakes

## Slide 21
Weston Solutions, Inc.
  SRA delineation
  Transect and grid detections used
  2,000 APA threshold
  Multiple SRAs identified across the site
    Largest in Demolition Area
    Navy bombing range to the east
    Not all munitions related
    Expect additional smaller SRAs
Former Boardman AFR
Remedial Investigation

## Slide 22
Weston Solutions, Inc.
  Can we do more?
  Understanding SRAs in RI stage can lead to better site characterization and anomaly density estimations
  Detections good for identifying SRAs but don’t tell the whole story
  EM 200-1-15 provides guidance for managing SRAs as part of RIs
    “such areas may require full excavation for cost estimating purposes or may only require sampling to identify the nature of the detected sources (i.e., munitions-related or not munitions-related)
  Not mentioned in QAPP Toolkit 1
  No plan for managing SRAs during RIs
Remedial Investigations
SRA Characterization

## Slide 23
Weston Solutions, Inc.
  Think beyond QAPP Toolkit 1 in the RI planning stage to develop methods for characterizing SRAs
    How SRAs will be defined and delineated
    Adequate intrusive sampling for characterization and more accurate density estimations
      Avoid costly anomaly reduction and remapping
      Modified mapping quality objectives (MQOs)
      Modified dig procedures
Saturated Response Areas
Conclusions

## Slide 24
Weston Solutions, Inc. 4
Weston Solutions, Inc.
Questions?
Trust. Performance. People.

## Slide 25
Contact Us
How can we best serve you?
Wendy Church, PG
Senior Project Geophysicist
Wendy.Church@westonsolutions.com
Mobile: 713-494-2581
Jake Vera
Project Geophysicist
Jake.Vera@westonsolutions.com
Mobile: 570-550-1660
Trust. Performance. People.
Weston Solutions, Inc. 4
Weston Solutions, Inc.
Kyle Yarmush
Senior Project Geophysicist
Kyle.Yarmush@westonsolutions.com
Mobile: 610-741-7755