## Slide 1
OPEN AIR TESTS OF COMPLEX SEED SCENARIOS TO BETTER UNDERSTAND IMPLEMENTATION AT MMRP REMEDIAL ACTION PROJECTS
Presented By: Andrew Fedetz
April 10, 2025
Trust. Performance. People.

## Slide 2
Data Usability Seed
Complex Seed Scenarios Key Concepts
Weston Solutions, Inc. 1
Two Scenarios:
Horizontal
  Place seeds within 40cm of emplaced clutter
Vertical
  Place clutter above seeds
Constraints:
No seed placed in physical contact or within 5cm of clutter
Depth distribution of anticipated MEC
Two to Four DU seeds per system per week
Seeding Purpose | Common Seeding Name | Primarily Performed By | Optional Performed By | Minimum Frequency | Design Specifications (all must meet TOI selection criteria)
Complex Seed Scenarios: Assess performance of the process to identify sources requiring excavation in the presence of nearby interference | Data Usability Seed (Can be counted as a QC seed) | Contractor | Government Lead Agent Federal or State Regulators (3rd party quality oversight) | AGC: Required minimum two to four per system per week Non-AGC DGM: Recommend minimum two to four per system per week. | Place some seeds within 40cm of emplaced clutter. Place clutter above some seeds. No seeds are placed in physical contact with, or within 5cm (~2 inches) of clutter. Depth distribution profile mimics that anticipated for MEC.
From EM 200-1-15 (Table 14-10)
Notes: Data usability seeds are complex seed scenarios where an ISO is emplaced co-located with a clutter item
From guidance document, my understanding is there are two complex scenarios: horizontal and vertical
Horizontal, clutter is placed at the same depth as the ISO within a range of offsets (5-40cm)
Vertical scenario, clutter is placed at the same horizonal x-y location, but shallower than the ISO (not within 5cm)

## Slide 3
Test Objectives
Clutter for Complex Seed Scenarios
Weston Solutions, Inc. 2
What is Clutter?
Assumptions:
Small metallic NMRD
Standardized for ease of logistics (Clutter ISO)
Classification results are Clutter invariant
Classification results are offset invariant
Notes: As a contractor, we need to evaluate what clutter is.
In the context of implementation on projects
  Standardization (type of clutter)
  Cost estimating (magnitude of items)
  Do we want to use MD as clutter? No, too many variables

## Slide 4
Collection Setup
AGC Cued MetalMapper2x2
Weston Solutions, Inc. 5
Horizontal Scenario:
Small and Medium ISO centered
  Horizontal offsets of clutter
  Repeated at different depths
Clutter centered
  Horizontal offsets of ISOs
  Repeated at different depths
Vertical Scenario:
Small and Medium ISO centered
  Vertical offsets of clutter above ISOs
  Repeated at different depths
Library
2.5in Rifle Grenade
Large ISO 40
Large ISO 80
Medium ISO 40
Medium ISO 80
Small ISO 40
Small ISO80
60mm Mortar
76mm HEAT
81mm Mortar
105mm Projectile
155mm Projectile
20mmTP Projectile with Cartridge
37mm Projectile
Horizonal Scenario schematic
Processing Parameters:
Processed in Seequent Oasis Montaj UXA 2024.1
Default parameters
0.825 TOI/Non-TOI threshold
Notes: Compare ISO classification results between clutter items
Identify scenarios with high passing MQO
How many RCAs?

## Slide 5
Clutter ISO
Standard Clutter for Complex Seed Scenarios
Weston Solutions, Inc. 3
Hex Nuts:
(2) 2.5 cm OD hex nuts zipped tied together
5/8 “ ID
Washers:
(4) 5 cm OD washers zipped tied together
3/4 “ ID
Thickness: ½” (1.27 cm)

## Slide 6
Clutter ISO
Standard Clutter for Complex Seed Scenarios
Weston Solutions, Inc. 4
Corner brace:
7.6 cm (3”) length corner brace
Aluminum Can:
Crushed 12 oz crushed can
9 cm length
Thickness: 2 cm

## Slide 7
 | Small ISO @ 7.6 cm (3-in) |  |  |  |  | Small ISO @ 15.2 cm (6-in) |  |  |  |  | Small ISO @ 22.9 cm (9-in) |  |  |  |  | Small ISO @ 30.5 cm (12-in) |  |  |  | 
Clutter Offset 10 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 32 |  |  |  |  | 22
Washer |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22
Corner Brace |  |  |  |  | 32 |  |  |  |  | 11 |  |  |  |  | 33 |  |  |  |  | 22
Crushed Can |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 11
Clutter Offset 20 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 11
Washer |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 30 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 32 |  |  |  |  | 22
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 40 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 22
Crushed Can |  |  |  |  | 33 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 50 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 32 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Crushed Can |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 22
Horizontal Scenario Results
Small ISO Centered
Weston Solutions, Inc. 6
Increasing depth BGS
Increasing clutter offset
Green = met MQO Red = failed MQO
Yellow = edge of MQO tolerance
  75% of HO tolerance (19 cm)
  75% of VO tolerance (11 cm)
  Decision Statistic between 0.825 – 0.90
Notes: Final Source list with default UXA values 0.825 TOI threshold
With ISO centered, almost all complex horizonal scenarios resulted in passing MQOs for small ISO classification
Miss classifications begin at 12 inch bgs. With corner brace and crushed can clutter items producing the most MQO failures
  Consistent with expectations of maximum reliable depth

## Slide 8
Horizontal Scenario Results
Small ISO; Clutter Centered
Weston Solutions, Inc. 7
Increasing ISO offset
 | Clutter @ 7.6 cm (3-in) |  |  |  |  | Clutter @ 15.2 cm (6-in) |  |  |  |  | Clutter @ 22.9 cm (9-in) |  |  |  |  | Clutter @ 30.5 cm (12-in) |  |  |  | 
ISO Offset 10 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 32 |  |  |  |  | 22
Washer |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22
Corner Brace |  |  |  |  | 32 |  |  |  |  | 11 |  |  |  |  | 33 |  |  |  |  | 22
Crushed Can |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 11
ISO Offset 20 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 11
Washer |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 22
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
ISO Offset 30 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 22 |  |  |  |  | 22 |  |  |  |  | 32 |  |  |  |  | 22
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
ISO Offset 40 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 32 |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 22
Crushed Can |  |  |  |  | 33 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
ISO Offset 50 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 32 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Crushed Can |  |  |  |  | 22 |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 22
Increasing depth BGS
Green = met MQO Red = failed MQO
Yellow = edge of MQO tolerance
  75% of HO tolerance (19 cm)
  75% of VO tolerance (11 cm)
  Decision Statistic between 0.825 – 0.90
Notes: Final Source list with default UXA values 0.825 TOI threshold
With cluttered centered, more MQO failures
Miss classifications begin at 12 inch bgs. With corner brace and crushed can clutter items producing the most MQO failures
  Consistent with expectations of maximum reliable depth and target offsets
  I would expect there to be recollects associated with larger offset measurements

## Slide 9
Horizontal Scenario Results
Medium ISO Centered and Clutter Centered
Weston Solutions, Inc. 8
Increasing clutter offset
 | Medium ISO @ 25 cm (10-in) |  |  |  |  | Medium ISO @ 50.8 cm (20-in) |  |  |  |  | Clutter Centered Medium ISO @ 25 cm (10-in) |  |  |  | 
Clutter Offset 10 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 21
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 20 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 31 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 30 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 31 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 11
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Clutter Offset 40 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Crushed Can |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 21
Clutter Offset 50 cm | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Washer |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 11
Corner Brace |  |  |  |  | 11 |  |  |  |  | 11 |  |  |  |  | 31
Crushed Can |  |  |  |  | 11 |  |  |  |  | 32 |  |  |  |  | 21
Increasing depth BGS
Green = met MQO Red = failed MQO
Yellow = edge of MQO tolerance
  75% of HO tolerance (19 cm)
  75% of VO tolerance (11 cm)
  Decision Statistic between 0.825 – 0.90
Notes: Medium ISO horizontal scenarios all pass MQO.
Seems to suggest relative size of ISO to clutter item plays large role in successful classification
  As expected

## Slide 10
Vertical Scenario Results
Small ISO
Weston Solutions, Inc. 9
Increasing ISO depth
Small ISO 15.2 cm (6-in) Clutter 7.6 cm (3-in) | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11
Washer |  |  |  |  | 22
Corner Brace |  |  |  |  | 21
Crushed Can |  |  |  |  | 33
Small ISO 22.9 cm (9-in) Clutter 7.6 cm (3-in) | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11
Washer |  |  |  |  | 22
Corner Brace |  |  |  |  | 22
Crushed Can |  |  |  |  | 22
Small ISO 22.9 cm (9-in) Clutter 15.2 cm (6-in) | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 32
Washer |  |  |  |  | 11
Corner Brace |  |  |  |  | 11
Crushed Can |  |  |  |  | 22
Small ISO 30.5 cm (12-in) Clutter 7.6 cm (3-in) | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 11
Washer |  |  |  |  | 22
Corner Brace |  |  |  |  | 22
Crushed Can |  |  |  |  | 22
Small ISO 30.5 cm (12-in) Clutter 15.2 cm (6-in) | HO | VO | Class | D Stat | Source
Hexnuts |  |  |  |  | 22
Washer |  |  |  |  | 11
Corner Brace |  |  |  |  | 33
Crushed Can |  |  |  |  | 11
Green = met MQO Red = failed MQO
Yellow = edge of MQO tolerance
  75% of HO tolerance (19 cm)
  75% of VO tolerance (11 cm)
  Decision Statistic between 0.825 – 0.90
Chart: Small ISO Vertical Scenario Total % MQO Pass/Fail
| ISO 15.2 cm Clutter 7.6 cm | ISO 22.9 cm Clutter 7.6 cm | ISO 22.9 cm Clutter 15.2 cm | ISO 30.5 cm Clutter 7.6 cm | ISO 30.5 cm Clutter 15.2 cm
Pass | 25 | 0 | 25 | 0 | 0
Edge | 50 | 0 | 50 | 0 | 25
Fail | 25 | 100 | 25 | 100 | 75
Notes: Small ISO Vertical scenario results show more MQO failures
Again, more MQO failures associated with corner brace and crushed can
Depth of clutter item seems to be dominant failure parameter
  Shallower clutter causing more MQO failures

## Slide 11
Vertical Scenario Results
Medium ISO
Weston Solutions, Inc. 10
Increasing ISO depth
Green = met MQO Red = failed MQO
Yellow = edge of MQO tolerance
  75% of HO tolerance (19 cm)
  75% of VO tolerance (11 cm)
  Decision Statistic between 0.825 – 0.90
Medium ISO 30.5 cm (12-in) Clutter 15.2 cm (6-in) | HO | VO | Classification | Decision Stat. | Source
Hexnuts |  |  |  |  | 11
Washer |  |  |  |  | 11
Corner Brace |  |  |  |  | 32
Crushed Can |  |  |  |  | 11
Medium ISO 50.8 cm (20-in) Clutter 7.6 cm (3-in) | HO | VO | Classification | Decision Stat. | Source
Hexnuts |  |  |  |  | 32
Washer |  |  |  |  | 33
Corner Brace |  |  |  |  | 21
Crushed Can |  |  |  |  | 32
Medium ISO 50.8 cm (20-in) Clutter 15.2 cm (6-in) | HO | VO | Classification | Decision Stat. | Source
Hexnuts |  |  |  |  | 21
Washer |  |  |  |  | 11
Corner Brace |  |  |  |  | 21
Crushed Can |  |  |  |  | 11
Medium ISO 50.8 cm (20-in) Clutter 30.5 cm (12-in) | HO | VO | Classification | Decision Stat. | Source
Hexnuts |  |  |  |  | 11
Washer |  |  |  |  | 11
Corner Brace |  |  |  |  | 11
Crushed Can |  |  |  |  | 11
Chart: Medium ISO Vertical Scenario Total MQO % Pass/Fail
| ISO 30.5 cm Clutter 15.2 cm | ISO 50.8 cm Clutter 7.6 cm | ISO 50.8 cm Clutter 15.2 cm | ISO 50.8 cm Clutter 30.2 cm
Pass | 75 | 0 | 0 | 50
Edge | 0 | 0 | 25 | 50
Fail | 25 | 100 | 75 | 0
Notes: Contrast to the horizontal scenario, where Medium ISO was classified in all tests
Again, more MQO failures associated with corner brace and crushed can
Depth of clutter item seems to be dominant failure parameter
  Shallower clutter causing more MQO failures

## Slide 12
Summary
Weston Solutions, Inc. 11
Horizonal Scenario
  Classification results are:
    Clutter type dependent (Crushed can most failures)
    Relative size of clutter item to ISO dependent
    Offset invariant
Vertical Scenario
  Classification results are dominated by depth of clutter
Chart: Combined Vertical Scenario % Pass/Fail MQO
| 7.6 cm (3-in) | 15.2 cm (6-in) | 30.5 cm (12- in)
Pass | 6.25 | 25 | 50
Edge | 12.5 | 25 | 50
Fail | 81.25 | 50 | 0
Chart: Small ISO Horizontal Scenario Total %MQO Pass/Fail
| Hexnuts | Washer | Corner Brace | Crushed Can
Pass | 87.5 | 78.125 | 65.625 | 65.625
Edge | 12.5 | 21.875 | 28.125 | 18.75
Fail | 0 | 0 | 6.25 | 15.625

## Slide 13
Weston Solutions, Inc. 4
Weston Solutions, Inc. 12
Questions?
Trust. Performance. People.

## Slide 14
 | HO | VO | Classification | Decision Stat. | Source
MISO 30.5 cm (12-in) SISO 15.2 cm (6-in) |  |  |  |  | 11
MISO 50.8 cm (20-in) SISO 7.6 cm (3-in) |  |  |  |  | 11
MISO 50.8 cm (20-in) SISO 15.2 cm (6-in) |  |  |  |  | 11
MISO 50.8 cm (20-in) SISO 30.5 cm (12-in) |  |  |  |  | 21
Bonus co-located MISO-SISO Vertical Scenario

## Slide 15
Weston Solutions, Inc. 13
Small ISO Vertical Scenario ISO 15.2 cm (6-in) Corner Brace7.6 cm (3-in)
Small ISO Vertical Scenario ISO 22.9 cm (9-in) Crushed Can 15.2 cm (6-in)

## Slide 16
Weston Solutions, Inc. 13
Medium ISO Vertical Scenario ISO 30.5 cm (12-in) Small ISO 7.62 cm (6-in)