## Slide 1: Innovative Background Noise Removal Technique for Underwater Target Detection and Classification
Fridon Shubitidze1,2, Maximilian A. Orman-Kollmar1, Irma Shamatava1,2
1Dartmouth College, Hanover, NH, USA, Fridon.Shubitidze@dartmouth.edu
2White River Technologies, Lebanon, NH, USA

## Slide 2: Problem Statement
Remediation and Detection of underwater UXO targets are more expensive than excavating the same targets on land
.
In the U.S. alone, an estimated 10 million acres of underwater areas may be contaminated with munitions.
These areas include lakes, rivers, estuaries, and coastal zones near active and former military sites.
In addition to conventional UXO, over 1.6 million tons of chemical weapons have been dumped in oceans worldwide since World War I.
Corroding munitions may leak toxic substances, such as mustard gas or white phosphorus, creating long-term environmental and ecological hazards.

## Slide 3
The Tx currents generate a primary magnetic field that penetrates the surrounding conductive medium and the metallic target.
The primary magnetic field is abruptly turned off, resulting in induced volume and surface currents within the conducting environment and the targets.
The induced currents produce secondary EM fields that are detected with a set of receivers
EMI sensing in an underwater environment

## Slide 4
EMI sensing in an underwater environment
The total field in Region 1 is the sum of the fields produced by the transmitter coil (response from water), reflected fields from boundaries, and fields from a target.
The total field in Region 2 is the sum of the transmitted fields and the response from a target.
During dynamic data collection mode, the Rx coils move within a time-varying magnetic field, resulting in additional motion-induced signals.
region 1
region 2

## Slide 5: EMI field of Tx coil in the Marine Environment
Magnetic field
The time derivative of the magnetic field
x
z
y
o
L
w
Tx
A Tx coil is placed in a conductive environment

## Slide 6: EMI Signals Induced in a Moving Rx Coil within Time Varying Field
Conductivity effect
Velocity effect
ULTRATEMA time window
ULTRATEMA time window
Notes: EMI Signals Induced in a Moving Rx Coil within a Time-Varying Field

## Slide 7
UltraTEMA: Single-Pass UW EMI detection and classification system
The UltraTEMA system consists of four transmitter coils and twelve vector receiver sensors. It measures complete EMI response of a target at each dynamic data point and provides 144 data value at each nth (n=1,2, .., 25) time gate.

## Slide 8
ULTRATEMA Operation principles

## Slide 9: Conductivity Profile
Conductivity S/m
Sequim Bay Calibration Area
2D Cross section
Along depth

## Slide 10: Data acquisition
A sensor is deployed in the marine environment.
The Tx/Rx coils traverse through various conductive layers.
The direct EMI signals from the Tx coils to the Rx coils are proportional to the conductivity of the medium.
Changes in yaw, pitch, and roll alter the orientation of the Tx/Rx coils, placing them in different conductive environments.

## Slide 11: Sensor noise
Comparisons between modeled and actual ULTRATEMA background noise data
A target’s signal
Signals due to sensor motion

## Slide 12: Detection maps
A combined gradient-based background removal technique.
UXO location
UXO location
A standard background removal.
Standard detrending technique: Zoomed-in EMI detection map centered on a UXO target within the Sequim Bay blind-grid
Gradient techniques: Zoomed in the ULTRATEMA EMI detection map centered on a UXO target within the Sequim Bay blind-grid

## Slide 13: Results: Single-Pass data processing
A set of dynamic data points is identified around the target.
An objective function is defined as the simple difference between two data points.
The target's location and classification features are extracted from each objective function.

## Slide 14
105 mm Projectile
Extracted effective polarizabilities
Results: Extracting Classification Features of Targets

## Slide 15: Scoring results
Rank | Easting | Northing | Dig
1 | 497802.13 | 5324503.49 | 1
2 | 497758.88 | 5324537.97 | 1
3 | 497801.99 | 5324494.04 | 1
… | … | … | …
52 | 497833.25 | 5324523.74 | 1
53 | 497771.66 | 5324546.91 | 0
53 | 497769.48 | 5324538.04 | 0
… | … | … | …
93 | 497810.67 | 5324570.99 | 0
Ranked Detection List Example
Likelihood of Being A UXO
All Detected Objects
Demonstrator’s
Dig Threshold
  93 detections, with 51 dig decisions
Processing steps:
  1. The detection map was created, and a list of detected anomalies was generated.
  2. Data points were extracted around each detected anomaly.
  3. Each data point was inverted to estimate the magnetic source(s) polarizabilities and locations. The extracted locations were then clustered, and polarizability within each cluster was combined.
  4. The cluster source locations were used as the estimated locations of anomalies, and the combined polarizabilities were used for classification.
  5. Anomalies were ranked using a library matching technique through automatic classification.

## Slide 16
Classification Summary Statistics
Halo Radius (m) | FP | FN | TP | Pdc
0.5 | 42 | 30 | 5 | 5
1.0 | 28 | 16 | 19 | 19
1.5 | 22 | 10 | 25 | 27
2.0 | 17 | 5 | 30 | 30
2.5 | 15 | 3 | 32 | 32
3.0 | 13 | 1 | 34 | 34
3.5 | 13 | 1 | 34 | 34
4.0 | 12 | 0 | 35 | 35
Best detection/classification performance happens at r= 4 m
Performance stabilizes, so ROC curve primarily reflects detection/classification rather than geolocation

## Slide 17: ROC Curves for high altitude data
High Altitude
Comparison between low and high altitude ROCs.

## Slide 18: Conclusions
An Innovative Background Noise Removal Technique has been developed.
The techniques applied to ULTRATEMA data sets collected at Sequim Bay at low and high elevations. a
All targets were identified as TOI.

## Slide 19: Acknowledgements
We would like to thank the ESTCP Office through project number MR23-9000.