## Slide 1
UAS Mag Surveys in Challenging Near Shore Environments
15 April 2025
Michael Gunnels | White River Technologies, Inc. | gunnels@whiterivertech.com

## Slide 2
Summary
WRT UAS-MAG Technology Overview
Reid State Park (Mar 2024)
  Site Prep and Flight Planning
  UAS Surveying
  Results
Other Technical Experiments
Conclusions

## Slide 3
Magnetometer
Notes: This is the core technology we’ll be talking about miniaturized magnetometers combined with medium sized UAS
Sensor is 1.4m from airframe center
Quick release to allow us to integrate sensor onto any platform with a servo rail

## Slide 4
UAS Airframe(s)
Custom
Cube-1000
Custom Cube-1000
  Octo-copter, ~1m wingspan
  20 min endurance
Blue Halo E-900
  Hexa-copter, ~90cm wingspan
  20 min endurance
BlueHalo E900
Notes: These are the two airframes that WRT uses depending on the application

## Slide 5
DroneMag Workflow
Site assessment
Mission Planning
MADCOM infield software
Infield processing
Analysis / Anomaly ID
• Pre deployment planning
• Site visit (if possible)
• ID of possible obstructions
Notes: Could shorten the bullet points,
WRT MAD COM infield software
Infield data processing (Filtering, QC, Detection,
Products: (GeoTIFFS, CSVs, PNGs, GeoJSON / JSON files)

## Slide 6
Reid State Park, Maine
Demonstration for ESTCP Phase I project
1-mile-long surf, beach, dunes, and marsh
Onsite for 8 days, IVS / seeding, 42 MAG sorties
Surf
Beach
Dunes
Marsh

## Slide 7: UAS Mission Planning
Careful pre-deployment planning of UAS sorties,
Split MRS up into 28 one-acre grids based on MQO line spacing requirement and UAS endurance
Missions were loaded onto field computer

## Slide 8
IVS and Seeding
QC Seeds (41 Total: 2 per grid)
IVS Seeds (4 items, 50m long)
Pre-install MAG Map
Initial MAG IVS Survey
MAG+APEX surveys
LG-ISOs, Cal Magnets
RTK-GPS Surveyed
We used APEX and APEX handheld to validate the LG ISO targets.
Notes: 2.25” rocket was the primary TOI

## Slide 9
Results: UAS Surveying
Each grid was ~ 1 acre
Completed 10 grids / day
Survey Days: 3
Notes: Mosaic detection map from 30 sorties showing a magnetic anomaly detection map over all of the MRS

## Slide 10
Results: UAS Surveying Performance
DAGPCAP style MQOs
1 million data points passed 2.5m spacing requirement
Cmd. altitude was 3.5m, sensor at 1.4m, < 2m MQO
Notes: We commanded the airframe to be 3.5m
Mag is therefore at 1.4m
Max altitude based on the main TOI at the site was 2m, so Percent A<2.0m AGL

## Slide 11: Results: Detection Performance
Notes: 3.5m up in the air,

## Slide 12: Results: Anomaly Density Estimates
Site wide target densities obtained on 30 acre site in ~ 3 days
Dipole detections used in VSP to estimate density

## Slide 13
Other Technical Experiments
Shell Island, FL – ESTCP Project (2023)
Technical Experiment with government stake holder (2024). Testing two sensor gradiometer.
Technical Experiment with government stake holder (2025)

## Slide 14: Results: Explosive Threat Detection
Approximately 7 sorties flown from both land and sea
Surf zone sortie flown from boat and landed on beach
Various metallic targets detection and localized

## Slide 15: Boat Ops
Performed 3 sorties from boat
Carried out survey over surf
Autonomous Landing on the shore

## Slide 16: Conclusions
Drone based magnetometry is an effective method for Wide Area Assessment, i.e., characterizing a large area to understand level of contamination or munition hazard throughout the area.
Careful mission planning will result in efficient data collection, accurate/reproducible line spacing, and precise altitude control across larger sites.

## Slide 17: Acknowledgements
Flight Crew and Team
  Dr. Greg Schultz,
  DB Bhowmick,
  Andrew Masters,
  Dr. Martin Helmke

## Slide 18: Backup Slides

## Slide 19: UAS Specs
Parameter | Specification
Drone Altitude (AGL) | 3.0-5.0 m
Sensor Altitude (AGL) | 1.1-3.1 m
Altitude Control | ±0.11 m
Waypoint Control | ±0.21 m
Survey Flight Speed | 3 m/s (5.8 kts)
Transit Flight Speed | 11.3 m/s (22 kts)
Sampling Rate | 200 Hz
Ground Sampling Distance | 3.75 cm
Detection/Report Rate | 0.25 Hz
Endurance | 30 min
Range | 3.5 – 4 km
Time-to-Anomaly Map | 60 sec
Time-to TOI Localization | 2 sec / TOI