## Slide 1: A Partnership between Environmental Remediation and Historical WWII Weaponry Preservation
Authors: Emily E. Snyder, Stuart Bancroft, Tessa Hermes, Dominique Jafar, Zach Wedgeworth, Gabe Chen, Jeremy Brunette, Brittney Mullins
LA-UR-25-22690

## Slide 2: Site Location
Historical, Manhattan Project Era site (1942-1946) on Los Alamos National Laboratory (LANL) property
Hummocky terrain in the SW corner
Steep terrain in the north portion of the planned survey area
Ponderosa pine, juniper, shrub oak, and tall grasses
Many artifacts still present onsite (pieces of metal of various sizes and concrete pads)

## Slide 3: Historical Background
Gun Site (1945-1946), a part of Technical Area (TA) 08, developed and tested gun-type weapon designs
In 1946, Material Disposal Area (MDA) Q was used as a disposal area for naval guns, inert projectiles and prototypes (nonnuclear), and expended casings
A 1993 geophysical survey identified an area at Gun Site that might contain MDA Q using geophysical surveys

## Slide 5: Why does this matter?
The scope was to identify the boundary of MDA Q using geophysical instrumentation
  This was in conjunction with the environmental remediation being conducted at this site, as well as the preservation of archaeological artifacts across the site
  The data collected from the geophysical instruments would support sample planners who needed to determine where to sample around MDA Q

## Slide 6: Geophysical Methods

## Slide 7: EM-61 and EM-31
5 ft spacing
Collected lines in a north-south orientation, alternating directions
Recording 10 readings/sec
Collected EM-61 data in differential mode and EM-31 data with in-phase and quadrature measurements

## Slide 8: GPR
2 ft spacing
350 MHz
Collected lines in a north-south orientation in addition to east-west transects. Both were done in alternating directions.
2 target areas were chosen from the whole site based on the EM survey results

## Slide 9: Data and Results

## Slide 10: EM-61
MDA Q identified – saturated area, not a single anomaly peak
Two anomalies specifically are related to the Naval gun mounts on the field site

## Slide 11: EM-61
MDA Q still present
Same anomalies shown in addition to some more
Additional anomalies present in Channel 2 not found in the Differential Channel likely represent small shallow anomaly sources

## Slide 12: EM-31
MDA Q identified
Concrete with rebar also seen

## Slide 13: EM-31

## Slide 14: GPR Profiles
Rapid signal attenuation between 3 -5 feet below ground surface
More frequent hyperbolic anomalies within MDA Q
No significant stratigraphic contrasts within MDA Q versus outside
Dipping reflection within vicinity of trees

## Slide 15: GPR Profiles

## Slide 16: GPR West Grid
Created a composite image of the data
No distinct anomalies present from aerial image or GPR profiles that were seen from the EM surveys

## Slide 17: GPR East Grid
Created a composite image of the data, but no distinct anomalies were noted
GPR profiles were also investigated and revealed more

## Slide 18: GPR Anomalies Picked
Picks selected a few feet from hyperbola peak and implemented a 5 ft buffer around each pick
Picks from the profiles in and around MDA Q
Picks around the tree we believe are dipping reflection related due to the tree roots

## Slide 19: Sample Locations
Avoided areas where picks were concentrated
Locations were selected around MDA Q and to a depth below it

## Slide 20: Conclusions
Both EM-61 and EM-31 surveys identified the MDA Q boundary
The GPR survey identified soil contrast throughout the site (~4-6 ft bgs)
This GPR data was used to determine sample locations that would avoid contact with objects in the subsurface around and beneath MDA Q

## Slide 21: Acknowledgements
N3B Los Alamos and Triad Cultural Monitoring Personnel
TPMC personnel for the field work, data processing, and illustrations
Funded by U.S. Department of Energy, Environmental Management Los Alamos Field Office (EM-LA)

## Slide 22: Questions

## Slide 23: GPR Profiles – Dipping Reflections