## Slide 1: Prototype Time Domain Transmitter for Sensing Carbon fiber, salt water, and landmines
Michele Maxson
Mikheil Prishvin
David Lozano
Max Orman-Kollmar
Fridon Shubitidze

## Slide 2: Outline
Problems and challenges
Current technologies
Background Physics
Early time EMI – design
Preliminary data
Conclusions

## Slide 3: Problems and challenges
1) LOW CONDUCTIVE MATERIALS
Landmines and Improvised Explosive Devices (IEDs) are usually constructed of plastic, wood, and rubber and contain very small amounts of metal
2) DEEP TARGET DETECTION AND CLASSIFICATION
Rule of thumb is that a target can be detected and classified by an AGC sensor at 11x it’s diameter.
Part of a damaged taxiway at Miyazaki Airport in southwestern Japan, Wednesday, Oct. 2, 2024, after an explosion was reported.

## Slide 4: Outline
Problems and challenges
Current technologies
Background Physics
TDLite – design
Preliminary data
Conclusions

## Slide 5: Current technologies
Advanced EMI Sensors (<100 kHz)
  Provide detection and classification for metallic objects
Magnetometers
  Only detects ferrous materials
Ground Penetrating Radar (50 MHz-3GHz)
  Detects metals as well as dielectrics
  High false alarm rate
Photo courtesy of United Nations Mine Action Service
Schonstedt
ULEMA H
CEIA CMD3
MineLab MDS10

## Slide 6: Outline
Problems and challenges
Current technologies
Background Physics
Early time EMI – design
Preliminary data
Conclusions

## Slide 7: Background physics
EM interacts with metallic target and induces volume/surface currents
Soils are “invisible”
Traditional EMI Frequency range: 10’s Hz up to 10’s KHz
Can detect and classify targets based on size and shape
Works for targets in soil, water, etc.
Notes: Explain how EMI works here

## Slide 8: Background Physics
Time range of most time domain sensors
Notes: Explain why we cannot detect low conductive targets with time domain systems here

## Slide 9: Background Physics
11 x diameter “rule of thumb” first referenced in 2006 (Survey of Munitions Response Technologies (UXO-4, 2006)) by the Interstate Technology and Regulatory Council
Based off EMI technologies to DETECT MOST SEEDED TARGETS
EMI platforms were EM-61 and GEM-3
Failed for “small: ordnance
20mm
Passed for “medium” and “large” ordnance
60mm
155mm
Figure 4-3. Predicted peak of the EM61-MK2 array anomaly amplitude in Gate 1 for a 4.2-inch mortar in its most favorable and least favorable orientations as a function of depth and measured values from a test pit adjacent and the GPO. Also shown are the system noise at the GPO and the detection threshold used for the EM61-MK2 array surveys.
Nelson, Herb, Katherine Kaye, and Anne Andrews. "ESTCP Pilot Program Classification Approaches in Munitions Response." ESTCP Web Site (2008).
Notes: Explain why we use 11x the diameter here
GPO = Geophysical prove out to verify detection threshold for an instrument. GPO; magnetometer was used to excavate then EM-61 cart was used to detect and excavate any more targets. The area was then seeded with 4.2” morters
https://www.frtr.gov/matrix-2019/documents/MEC-Screening/2006-Survey-of-Munitions-Response-Technologies.pdf

## Slide 10: Outline
Problems and challenges
Current technologies
Background Physics
Early time EMI – design
Preliminary data
Conclusions

## Slide 11: TDLITE design
Power Control does not have pulse width modulation
Integrated Half-Bridges
Shutoff Time: Faster –approximately 2mS (Smaller Inductances)
Power Dissipation: Coil-Based

## Slide 12: Outline
Problems and challenges
Current technologies
Background Physics
Early time EMI – design
Preliminary data
Conclusions

## Slide 13: Comparison to metal shotput
ULEMA operating range
Early time
EMI
operating range
~x21
Notes: Make a note here that the earliest that the TDLite sees has a signal which is 21x larger than the earliest ULEMA.
This implies we may be able to see 1.5x deeper (i.e 1/(6th root of 21)).
This may increase the total depth of detection from 11x to 16.5x the target diameter (11x1.5)

## Slide 14: Comparison to Carbon fiber Sphere
ULEMA operating range
Early time
EMI
operating range

## Slide 15: Comparison to Carbon fiber plate
ULEMA operating range
Early time
EMI
operating range

## Slide 16: Comparison to salt water

## Slide 17: VS50 Anti-personnel mine
ULEMA operating range
Early time
EMI
operating range

## Slide 18: Outline
Problems and challenges
Current technologies
Background Physics
Early time EMI – design
Preliminary data
Conclusions

## Slide 19: Conclusions
Early time EMI system provides a faster shut off time than other time domain systems
Early time EMI transmitter coil has been optimized to produce a large magnetic field and to collapse the primary magnetic field “bubble” quickly.
Fast shut off times allow for detection of targets with lower conductivity values
Fast shut off times allows for deeper target detection
Need to redesign the receiver coils to maximize the received field captured at early time
Amplifiers need to be optimized for the recovery time at early time
May create multiple receiver coils to capture the signal in both “early” time and “normal” time

## Slide 20
Special thanks to:
Dr. Fridon Shubitidze
Professor of Engineering
Dartmouth College
Thayer School of Engineering
Fridon.Shubitidze@dartmouth.edu
603-646-3671