## Slide 1: Impacts of Latency on Temsense One-pass Classification Results
Brian Junck M.Sc.
Senior Geophysicist

## Slide 2: Project Background
Remedial Design - Initially two-pass technical approach
  Morphed into One-pass
  Some two-pass MQOs preserved
Temsense one-pass on 113 grids
  RTK and SLAM positioning
IVS data for 82 days
Data Processing
  Initial processing performed using a modified workflow in v2021.2.1
  Final processing performed in v2023.1.1 using One-pass workflow

## Slide 3: Project Background
9 Seed Failures
  QC Seeds all targeted < 0.25m
  QC Seed Classification Failures
    (3) Decision Statistic < 0.825
    (6) Fit Coherence < 0.80
    (1) Fit Location > 0.25m
    No depth failures
  Daily IVS MQOs pass
  Ongoing SFTs Pass
  No obvious issues with production data (speed, coverage, etc..)
  Data levelling/filtering appropriate

## Slide 4: Seed Classification Details
Grid ID | Positioning | Seed Type | Orientation | Depth (m) | Decision Statistic | Fit Coherence | Source Offset (m) | Predicted Source Type
G002 | SLAM | Small ISO80 | Horizontal | 0.20 | 0.91 | 0.75 | 0.05 | Small ISO80
G003 | SLAM | Small ISO80 | Horizontal | 0.17 | 0.95 | 0.75 | 0.06 | Small ISO40
G006 | SLAM | Small ISO80 | Horizontal | 0.25 | 0.93 | 0.76 | 0.06 | Small ISO40
G007 | SLAM | Small ISO80 | Horizontal | 0.23 | 0.98 | 0.65 | 0.27 | Small ISO80
G085 | RTK | Small ISO80 | Vertical | 0.15 | 0.80 | 0.92 | 0.07 | Small ISO40
G089 | RTK | Small ISO80 | Vertical | 0.23 | 0.69 | 0.94 | 0.14 | none
G096 | SLAM | Small ISO80 | Horizontal | 0.16 | 0.94 | 0.79 | 0.05 | 37mm Projectile
G098 | SLAM | Small ISO80 | Horizontal | 0.19 | 0.83 | 0.67 | 0.08 | Small ISO80
G100 | RTK | Small ISO80 | Vertical | 0.18 | 0.80 | 0.97 | 0.07 | MK IV Booster

## Slide 5: Root Cause Analysis
Data Review
  Initial Evaluation and Tests
    No indicators of latency issues based on IVS MQO review
    data chip size + increasing number dipoles
      Corrected majority of seed failures, but not all
  Deeper dive into IVS and latency
    Method of latency assessment
    Routine to assess latency at 0.01 sec increments
  Indicators
    Fit Coherence (Fit_Coh)
    Library Match (LmStat_111toi)

## Slide 6: IVS Configuration
Initial IVS results
  IVS configuration
    Two Small ISO80
      1 Horizontal Cross-line
      1 Horizontal Along-line
    Daily collection of 3 passes
      1 seed lane
      2 offset
      1 noise lane
  Passing detection
    Ongoing < 0.25m offset
  Passing classification results
    Ongoing >0.90 LmStat, >0.80 Fit Coh

## Slide 7: IVS Configuration
    Latency: -0.13
    Match Metric: 0.98
    Fit Coh: 0.96
    Latency: 0.00
    Match Metric: 0.98
    Fit Coh: 0.92
    Latency: 0.05
    Match Metric: 0.98
    Fit Coh: 0.90

## Slide 8: IVS Latency Assessments
RTK Latency – ISO01
SLAM Latency – ISO01

## Slide 9: IVS Latency Assessments
RTK Latency – ISO02
SLAM Latency – ISO02

## Slide 10: Grid Latency Assessments – Horizontal QC Seeds
Grid G003 - SLAM
  SMISO80 – Horizontal
  Wide latency window
  Match Metric > FitCoh
  DS ~= Match Metric

## Slide 11: Grid Latency Assessments – Horizontal QC Seeds
Grid G006 - SLAM
  SMISO80 – Horizontal
  Wide latency window
  Match Metric > FitCoh
  DS ~= Match Metric

## Slide 12: Grid Latency Assessments – Vertical QC Seed
Grid G100
  SMISO80 – Vertical
  Narrow latency window
  Match Metric < FitCoh
  DS ≠ Match Metric

## Slide 13: Production Grid Corrective Action
Revised latencies applied to production data
  RTK: -0.13 sec
  SLAM: -0.45 sec
Data reprocessed and reclassified
  v2023.1.1 using one-pass workflow
  QC Seeds pass

## Slide 14: Conclusions
One-pass classification (2x2 Array Geometry)
  Small latency adjustments make a large impact on classification
  Vertical ISO
    Narrower acceptable latency window
  Horizontal ISO
    Generally wider latency window
  General comments
    Good practice to include a vertical ISO in IVS
    QC Seeding program should include vertical ISOs
    Perform quantitative latency assessment of IVS – not just an ‘eyeball’ test